TOYOTA

Press Information

FOR IMMEDIATE RELEASE

March 25, 1992

TOYOTA CELICA TURBO 4WD CARLOS SAINZ

In developing this latest version of the Celica GT-Four, Toyota set out to provide Toyota Team Europe (TTE) and its leading drivers, Carlos Sainz and Markku Alen, with reliable and ultra-competitive machinery with which to contest the 1992 World Rally Championship.  The previous GT-Four rally car had already set the highest standards, winning five championship rallies last year and five more in 1990, the year in which Spaniard Carlos Sainz lifted the World Championship.

In homologating the Celica Turbo 4WD Carlos Sainz for international rally competition, Toyota had to produce 5000 examples of which 3000 have been allocated to Europe and of these, only 440 are available in the UK.

The car obviously had to be relatively easy to convert into an effective rally machine, capable of winning in the snow and ice of Europe as well as the heat, dust and mud of Australia, Argentina and Kenya.  Considerable attention was therefore paid to keeping the engine and turbocharger cool as well as to the suspension.

But for the road-going version of this already successful rally car, great comfort, practicality and easy driveability were top priorities as well as performance.

The Turbo 4WD Carlos Sainz is instantly recognisable from its redesigned front bumper and air dam which not only looks very purposeful, but also allows adequate cooling air to reach the water and oil radiators.   Front  fog  lights  (standard on the GT-Four) are not fitted.  The bonnet is also a new body pressing with a small air inlet specifically to cool the engine timing belt and three separate air outlet ducts designed to evacuate hot air from the engine compartment.  At the rear, the bumper has also been redesigned to reduce weight and there are small change to the rear light clusters.

The 3S-GTE 2.0-litre engine with 16 valves and twin overhead camshafts is largely unchanged, but the turbocharger now features a water (instead of air) cooled intercooler increasing power from 201 to 205 bhp at 6000 rpm.  To improve heat dissipation in the valve area next to the valve seat, the 3S-GTE cylinder head uses the world's first laser-clad seats.  Welded by laser beam, the one-piece structure allows heat to dissipate more evenly.  Although peak torque remains the same at 203 lb ft, the characteristics have changed to give a much flatter torque curve for even better mid-range performance.  As a further aid to engine cooling, the electronic radiator fan power has been increased from 120 watts to 160 watts.

Underneath, the oil sump protector has been redesigned to save more weight and is now welded to the chassis centre member.  In a further effort to reduce weight, the exhaust system is not fitted with a dynamic damper and the rear exhaust silencer has been changed to reduce pressure loss and add a sportier exhaust note. Noise, vibration and harshness have been reduced though, by fitting a dynamic damper to the central prop shaft of the four wheel drive transmission system.

To make for even quicker gear changes, the clutch stroke has been reduced from 145 mm to 125 mm and the gear lever throw has been  reduced from 68 mm to 55 mm.

The Celica GT-Four already has a fine reputation for stability, exceptional grip and outstanding handling but, for the Carlos Sainz version, the suspension came under renewed scrutiny.  MacPherson struts are retained front and rear but the dampers are new and reduce friction.  At the front, Vorlauf geometry is used,  the kingpin offset is reduced and the lower L arms are anchored to a front chassis member for greater rigidity.  There is now greater negative camber at the rear and the dampers include valves which allow them to effectively damp even very low velocity wheel shocks.  Straight line stability, cornering and handling characteristics are all improved by these apparently small but important changes.

Elsewhere, the rigidity of the steering column has been increased with a new rubber coupling on the intermediate shaft.  The centre differential of the 4WD transmission now incorporates a viscous coupling,  and a torque sensing  (Torsen) LSD continues to be used at the rear.   This LSD consists of two worm gears and six worm gears with spur gears on them.  These use gear friction to create bias and, with a higher bias than conventional LSDs, the time lag is shorter.  Not only does the Torsen differential split torque left and right, but it makes it possible for accomplished drivers to control the torque split with adroit use of the accelerator.

Further improvements to the transmission include triple cone synchro on second gear and double cone synchro on third for improved durability and ease of shifting. Inside, the Celica Turbo 4WD Carlos Sainz is identified by a special numbered plaque on the centre console bearing Sainz's signature.  The steering wheel has a thicker leather cover, and the shorter throw gear lever and knob are a new design.   New cloth trim is practical as well as sporty, and a coin slot on the console is convenient for loose change.

Like the Celica GT-Four, the Carlos Sainz version has the kind of luxury features a rally driver would love to have.  Air conditioning, and electric sunroof, electric windows and central locking  are all there along with a six-speaker RDS stereo  radio and cassette system.  The steering wheel is tilt adjustable and steering is power assisted.  A three-way catalytic converter is standard.

TOYOTA CELICA TURBO 4WD CARLOS SAINZ

Technical Specification

ENGINE				3S-GTE 4 cylinder, in-line. Turbocharger

with water cooled intercooler

Valve mechanism			4 valves per cylinder. DOHC

Bore and stroke			86 mm x 86 mm

Capacity				1998 cc

Compression ratio			8.8:1

Fuel system				Electronic fuel injection

Fuel type				95 RON unleaded (3-way catalytic converter)

Ignition				Transistorised

Power output				205 bhp at 6000 rpm

Torque				203 lb ft at 3200 rpm

Battery				12V 48 amp hr

Alternator				12V 80A

Maximum speed				143 mph

0-60 mph					7.6 secs

0-400 m					15.4 secs

Speeds in gears -

1st						34.8 mph

2nd						61.5 mph

3rd						93.8 mph

4th						128.6 mph

Fuel consumption- urban

23.3 mpg (12.1 litres/100 km)

56 mph 37.7 mpg (7.5 litres/100 km)

75 mph 30.1 mpg (9.4 litres/100 km)

Towing capacity with/			1200 kg/600 kg

without brake

Fuel tank capacity				68 litres

DIMENSIONS

Length					4425 mm

Width						1745 mm

Height						1300 mm

Wheelbase					1475 mm

Track						1445 mm

Overhang					Front     1000 mm

Rear       900 mm

Ground clearance				150 mm

Kerbweight 					Front		910 kg

Rear		610 kg

Total		1520 kg

Gross vehicle weight 			Front		1015 kg

Rear		875 kg

Total		1890 kg

Cd 						0.35

TRANSMISSION

Clutch						Diaphragm spring, single plate

Transaxle type				E151F

Ratios

1st						3.583

2nd						2.045

3rd						1.333

4th						0.972

5th						0.731

Reverse					3.545

Diff ratios					Front		3.933

Centre	0.341

Rear 		2.928

Rear diff					Torque Sensing Type

SUSPENSION

Front and rear				MacPherson struts with anti-roll bars

Spring rate					Front		30.0 N/mm

Rear		28.5 N/mm

Anti-roll bar front/rear			Torsion, 27 mm dia/l8 mm

BRAKES

Front 						Ventilated discs 277 mm dia with tandem

7 in x 9 in servo assistance

Rear 						Discs 288 mm dia with tandem

7 in x 9 in servo assistance

Parking brake				170 mm drum acting on rear

STEERING

Ratio						Rack and pinion 16.8:1,  2.7 turns lock to lock

Power assistance				Spool Valve

Turning circle (tyre)   			11.0 m

Front toe-in					0 mm

Front camber   				-10’

Castor   					1° 10’

WHEELS AND TYRES

215/50 VR 15 Dunlop on 15 x 6.5jj

alloy wheels

TOYOTA CELICA TURBO 4WD CARLOS SAINZ

Standard Equipment

Alloy wheels

Front and rear mudflaps

Colour keyed bumpers and door mirrors (electrically adjusted)

Headlamp washers

Tinted glass with laminated screen

Rear wash wipe with intermittent

3-speed wipers plus variable intermittent

Rear spoiler

Locking fuel filler with internal release

Electric aerial

Illuminated boot with tool kit

Heated rear window

50/50 split rear seats

Inertia reel seatbelts

Electronic stereo radio cassette with RDS, Dolby, 18 pre-set

stations and six speakers

Centre console/armrest with cassette storage

Cigarette lighter

Cup holder

Illuminated, lockable glove box

Sun visors with vanity mirror

Central locking

Electric windows

Tilt and slide electric sunroof

Map light

Digital clock

Panel light rheostat

Cockpit headlamp adjustment

Push button heater/ventilation controls with four speed blower

Internal releases for bonnet and boot

Tilt adjustable steering column

Passenger grab handle

Full carpeting

Cloth velour upholstery

5-way adjustable driver's seat

Lights-on audible warning

ABS braking

Power steering

Air conditioning

Leather rimmed steering wheel

Memory tilt away steering column

3-way catalytic converter